One of the world’s smallest non-contact temperature sensors now available in the UK from Micro-Epsilon

A non-contact infra-red temperature sensor that is ideal for measuring temperatures in industrial environments, is now available in the UK through precision sensor manufacturer Micro-Epsilon.

For plant engineers, maintenance technicians, field and service engineers, the Optris® CT temperature sensor is ideal for use in automation, mechanical systems, control engineering, plant construction environments and can measure temperatures from -40°C up to 900°C, with a temperature resolution of 0.1°C within 160 milliseconds. The unit has an optical resolution of 2:1, 15:1 and 20:1 (as standard). The standard unit is able to withstand ambient temperatures of up to 180°C without cooling.

The latest developments allow a very small spot size by using a miniaturised sensing head, measuring just 28mm in length and an M12 diameter connecting thread. The optical nature of the measurement principle enables the engineer to aim and focus the sensor head at the target to give a specific ‘spot size’. With the help of a micro-lens, which can be installed in front of the integrated lens, the user is able to measure objects that have a diameter of just 0.6mm.

The products can be protected by mounting them in air purge collars. A new, innovative ‘right angle’ air purge collar allows a laminar flow of air across the front face of the sensor to maintain the sensor at constant temperature, but does not cool the target – a common problem with conventional cooling systems.

The sensor electronics are located separately in a die cast enclosure rated to IP67. The set up of the electronics is via a membrane pad fitted to the controller as standard, and can also be carried out via USB, RS232 or RS485 interfaces. In one customer application, an RS485 protocol, customised for time-critical applications, enabled measurements of up to 64 bus-connected sensors within 50 milliseconds.

- ENDS -

Note to Editors: Optris (www.optris.com) is a wholly-owned subsidiary of Micro-Epsilon. The company is based in Berlin, Germany and specializes in the development, production and sales of contactless infra-red thermometers. The product range comprises online sensors, portable infra-red cameras and pyrometers, which are used for maintenance and process control.

Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of sensors measure everything from displacement to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include inductive, differential transformer, eddy-current, capacitive, laser-optical, potentiometric and draw-wire principles.

With more than 30 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its clients.

| For more information or high resolution images, please contact: |
| --- |
| ENQUIRIES |  |
| Chris Jones | Tel (Office): 0151 482 5545 |
| Managing Director | Tel (Mobile): 07789 484503 |
| Micro-Epsilon UK Ltd | e-mail: chris.jones@micro-epsilon.com |
| DBH House, 105 Boundary Lane | Website: www.micro-epsilon.co.uk |
| Liverpool L5 9YJ |  |

# Text boxes

#### Ref. ME16									9th December 2005