# Low cost hand-held thermometer device measures temperatures from –35°C up to 900°C

A hand-held, infra-red temperature measurement device has been developed that enables engineers to measure the surface temperature of objects down to 1mm in size. The unit is accurate to ±0.75% and so provides plant engineers, maintenance technicians and field and service engineers with an attractive lower cost alternative to using thermal cameras.

The optical resolution of Micro-Epsilon’s ‘Optris® LaserSight’ device is 75:1, therefore users can measure smaller targets that are further away. Most competing products on the market only use an 8:1 ratio.

The 75:1 resolution is achieved by a world-wide patented laser sighting with special, narrow beam aiming. The new laser crosshairs sighting system supports precise temperature measurements at any distance. The crosshairs exactly mark a measuring spot in its real size of 16mm at a distance of 1.2m.

The measuring range of the device is from –35°C up to 900°C. The unit also benefits from a slimline, ergonomic design and is no larger or heavier than a standard TV remote control device, and so fits neatly into an engineer’s pocket.

A switch helps shift into a ‘close focus’ mode: two single laser beams cross each other at the smallest measuring spot.

An integrated position sensor flips the LCD display into the most convenient viewing position, so the LaserSight can be used in vertical or horizontal measuring mode. This makes the device ideally suited to measuring manifold temperatures.

A USB interface and graphics and reporting software with oscilloscope functionality helps to process and record up to 20 measurements per second. The device comes with a tripod mounting, a type K thermocouple, a padded soft pouch and carrying case.

The Optris® LaserSight is ideally suited to preventive maintenance applications, quality management, research and development and electronic design.

290 words					- ENDS -

Note to Editors: Optris (www.optris.com) is a wholly-owned subsidiary of Micro-Epsilon. The company is based in Berlin, Germany and specializes in the development, production and sales of contactless infra-red thermometers. The product range comprises online sensors, portable infra-red cameras and pyrometers, which are used for maintenance and process control.

Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of sensors measure everything from displacement to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include inductive, differential transformer, eddy-current, capacitive, laser-optical, potentiometric and draw-wire principles.

With more than 30 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its clients.

| For more information or images, please contact: |
| --- |
| ENQUIRIES |  |
| Chris Jones | Tel (Office): 0151 482 5545 |
| Managing Director | Tel (Mobile): 07789 484503 |
| Micro-Epsilon UK Ltd | e-mail: chris.jones@micro-epsilon.com |
| DBH House, 105 Boundary Lane | Website: www.micro-epsilon.co.uk |
| Liverpool L5 9YJ |  |

# Text boxes

#### Ref. ME18										4th November 2005