New two-wire loop powered infrared temperature sensor from Micro-Epsilon

Micro-Epsilon has expanded its range of non-contact infrared temperature sensors to include a new programmable, two-wire loop powered version.

The new thermoMETER CSmicro 2W sensor is a 4-20mA loop-powered device that measures temperatures from –30 deg C up to 1,600 deg C. The processing electronics are integrated in the cable itself, making the sensor one of the most compact, high accuracy, programmable pyrometers available on the market today.

Other sensors of a similar size currently available on the market do not have in-built processing/conditioning electronics to linearise the sensor output. This means the user has to linearise the output himself, which can be complex and time consuming.

With rugged silicon coated optics (15:1 or 75:1), the thermoMETER CSmicro 2W offers a system accuracy of ±1.0% and ± 0.3% of the reading respectively. The sensor can be used in ambient temperatures of up to 130 deg C without having to cool the sensor head.

A two-wire loop powered sensor extracts the power it needs to operate its electrical circuits from the loop itself. There is no separate power feed from the analogue input card or from anywhere else. The current that the device draws becomes part of the 4-20mA that flows in the loop, therefore the device does not require more than 4mA to operate. This means the number of wires and connections are reduced. Two-wire loop powered sensors are predominantly used by the process manufacturing industry, including oil and gas, petrochemicals, chemicals and power generation companies.

With the thermoMETER CS micro 2W, an optional USB connection and Micro-Epsilon’s CompactConnect software enable the user to set up and configure the sensor or to change the emissivity to suit the target material. The USB interface enables the user to connect to a PC or laptop in order to configure the temperature range and output span of the sensor or to download new parameters. The free software includes analysis functions such as a graphical display that shows temperature trends and enables automatic data logging for analysis and documentation.

For more information on Micro-Epsilon’s thermoMETER CSmicro 2W, please call the sales department on 0151 355 6070 or email: info@micro-epsilon.co.uk

– ENDS –

Note to Editors: Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of displacement sensors measure everything from to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include 1D, 2D and even 3D laser-optical sensors and systems, eddy-current, capacitive, LVDT & inductive, potentiometric and draw-wire principles.  Additionally Micro Epsilon has developed its own range of non-contact infrared temperature sensors that can measure virtually any target temperature from -40 to +3,300°C.

With more than 30 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its customers.

To download high resolution images for this article, please go to the “Press Area” at www.silverbulletpr.co.uk . Alternatively, you can request an image by contacting:

Issued by:			Dean Palmer

Director

SilverBullet PR Ltd

The Grey House, 3 Broad Street, Stamford,

Lincolnshire PE9 1PG

Tel: 01780 753 000

Mobile: 07703 023771

Email: dean@silverbulletpr.co.uk

Reader Enquiries/Advertising:	Chris Jones
				Managing Director

Micro-Epsilon UK Ltd

Unit 1
Pioneer Business Park
North Road
Ellesmere Port
Cheshire CH65 1AD

Tel: +44 (0) 151 355 6070
Fax: +44(0) 151 355 6075

Mobile: 07789 484503

Email: chris.jones@micro-epsilon.co.uk

# Text boxes

#### Ref. ME87									            29th September 2009