Draw-wire sensors used for wind turbine rotor blade testing

Draw-wire displacement sensors from Micro-Epsilon are playing a vital role in the testing of the latest generation of wind turbine blades at the Fraunhofer Institute in Bremerhaven, Germany.

The test rig at the Fraunhofer Institute simulates the distortion of rotor blades due to the effects of wind forces. The tip of the rotor blade can be distorted by up to 10m due to mechanical loads. The rig is designed to measure rotor blades up to a length of 70m.

During tests, the rotor blade itself is mounted horizontally in the test rig. Steel cables are attached to the rotor using guide pulleys and fixed to the rotor blade at various positions along its length, either directly or via mechanical clamps. Twelve draw-wire sensors from Micro-Epsilon are used to measure the distortion.

Two draw-wire sensors for each cable are mounted to the rails on the floor. These sensors measure the movement and the distortion of the rotor blade. The P115 sensors are from Micro-Epsilon’s wireSENSOR range and have measuring ranges of between 3m and 10m. The sensors operate with a digital output signal and are particularly robust due to their aluminium housing.

The principle of a draw-wire displacement sensor is relatively straightforward, hence its inherent reliability. A draw-wire sensor works rather like a tape measure, except the user does not have to read off the measurement of the extended tape. The rotation of the drum on which the steel wire is wound is measured automatically. The drum itself incorporates a long-life spring drive, which ensures the steel wire is rewound.

Chris Jones, Managing Director at Micro-Epsilon (UK) Ltd comments: “In addition to wind turbine testing, our draw-wire sensors are being used in a wide range of applications, from general industrial machinery and scissor lifts, through to more specific uses such as dentist chairs, patient lifting tables, theatre stages, pneumatic and hydraulic systems, aircraft landing gear and forklift trucks. Our wireSENSOR range is proving very popular with UK machine builders and OEMs, who require low cost, robust, reliable sensing solutions that can be easily integrated into their customer’s existing machine, components or control and automation systems.”

The wireSENSOR range uses three main measurement methods: a multi-turn potentiometer, an incremental encoder or an absolute encoder. One of these devices is mounted onto the drum axle, converting the rotary motion of the drum into a signal that can be evaluated. The measured displacement can be output as an analogue current, voltage or potentiometric signal. For a digital output, there is a choice of HTL or TTL, with interfaces for most of the common fieldbus systems, including CANopen, SSI and Profibus.

As with traditional tape measures, the wireSENSOR series is capable of measuring around corners and edges. Micro-Epsilon supplies as accessories deflection pulleys, which deflect the steel wire in the desired direction.

For more information on Micro-Epsilon’s range of draw-wire sensors, please call the Micro-Epsilon sales department on 0151 355 6070 or email: info@micro-epsilon.co.uk

– ENDS –

Note to Editors: Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of displacement sensors measure everything from to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include 1D, 2D and even 3D laser-optical sensors and systems, eddy-current, capacitive, LVDT & inductive, potentiometric and draw-wire principles.  Additionally Micro Epsilon has developed its own range of non-contact infrared temperature sensors that can measure virtually any target temperature from -40 to +3,300°C.

With more than 30 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its customers.

To download high resolution images for this article, please go to the “Press Area” at www.silverbulletpr.co.uk . Alternatively, you can request an image by contacting:

Issued by:			Dean Palmer

Director

SilverBullet PR Ltd

The Grey House, 3 Broad Street, Stamford,

Lincolnshire PE9 1PG

Tel: 01780 753 000

Mobile: 07703 023771

Email: dean@silverbulletpr.co.uk

Reader Enquiries/Advertising:	Chris Jones
				Managing Director

Micro-Epsilon UK Ltd

Unit 1
Pioneer Business Park
North Road
Ellesmere Port
Cheshire CH65 1AD

Tel: +44 (0) 151 355 6070
Fax: +44(0) 151 355 6075

Mobile: 07789 484503

Email: chris.jones@micro-epsilon.co.uk

# Text boxes

#### Ref. ME89									            15th October 2009