October 2006

The ‘bible’ of rolling bearings

Schaeffler UK has launched a new, 1500-page rolling bearing catalogue, which not only includes more than 40,000 INA and FAG products, but also provides design engineers with a comprehensive ‘bible’ of technical knowledge and bearings expertise.

The new ‘rolling bearings’ catalogue from Schaeffler (UK) is more than just a catalogue of the company’s vast range of 40,000 rolling bearing products. More than 140 pages are devoted to the technical principles of rolling bearings, helping design engineers size and select the correct bearings for their intended application.

The 1,500-page catalogue replaces seven individual product catalogues. Bearing product sections include deep groove ball bearings; angular contact ball bearings; cylindrical roller bearings; spindle bearings; bearings for screw drives; track rollers; housed bearing units; tapered roller bearings; needle roller and cage assemblies; spherical roller bearings; drawn cup needle roller bearings; bearing housings and accessories.

The ‘technical principles’ section of the catalogue includes information on fatigue theory; dynamic and static load carrying capacities of bearings; variable loads and speeds; life ratings; rigidity and deflection; friction values; limiting speeds and thermally safe operating speeds; lubrication principles; design of bearing arrangements; and information on fitting and dismantling.

This section of the catalogue will enable design engineers to decide which products they are able to use for an application; what they need to consider when designing the bearing arrangement; which tolerances are suitable for the adjacent construction; and how they can achieve the most effective sealing of their bearing arrangement. It will also help designers calculate the rating life of the bearings; what temperatures and loads can be supported; which lubricants are most suitable for the bearing arrangement; how and when maintenance should be carried out; and how to install and fit the bearings.

“The new joint branded catalogue is another important step in our one-face-to-the-customer strategy, and demonstrates further how the two brands of INA and FAG perfectly complement each other,” commented Kate Hartigan, managing director at Schaeffler (UK).

The catalogue is user-friendly and is an essential reference work for design engineers, OEMs, distributors and end users. All the company’s latest technical developments are covered in the compendium. For a copy, please visit www.schaeffler.co.uk or telephone the marketing department on 0121 351 3833.

ENDS

Note to editors:

With a total of 60,000 employees at over 180 locations around the globe and group sales of 8 billion euros (fiscal year 2005), the Schaeffler Group is one of the world's leading rolling bearing manufacturers and automotive component suppliers. The corporate group includes the INA Group with headquarters in Herzogenaurach, the FAG Group based in Schweinfurt as well as the LuK Group, with headquarters in Bühl.

FAG Industrial Services (FIS) is a member of the FAG Group and supports INA FAG in the UK and worldwide with industrial services including effective maintenance management and condition monitoring.

To download a high resolution image for this article, please go to the “Press Area” at www.silverbulletpr.co.uk . Alternatively, you can request an image by contacting:

Dean Palmer

Director

SilverBullet PR Ltd

Tel: 07703 023 771

Email: dean@silverbulletpr.co.uk

www.silverbulletpr.co.uk

Schaeffler (UK) Ltd,

Forge Lane

Minworth

Sutton Coldfield

West Midlands B76 1AP

Tel:   0121 351 3833	Fax:  0121 351 7686
e-mail: ina-fag@uk.ina.com	www.schaeffler.co.uk