| Date |  |
| --- | --- |
| 24th September 2020 | Page 1 of 1 |

# For immediate release

New robust, maintenance-free LED floodlights from Glamox offer high light output, long lifetime and easy installation

Global LED lighting specialist Glamox has introduced a new range of LED floodlights for safe areas in marine and offshore applications. The floodlights provide high light output, durability and a long system lifetime.

The FL70 range of LED floodlights are designed using the latest COB LED light source and LED driver technology, providing a virtually maintenance-free lighting solution. The floodlights are suitable for all high and medium intensity lighting requirements, with light outputs available from 27,000 up to 54,000 lumen.

Following thorough heat conduction and heat dissipation simulations, the floodlight design and components, including a powder-coated anodised seawater-resistant aluminium housing, are optimised for harsh marine and offshore conditions, ensuring a long lifetime of 100,000 hours (L70B50).

7 different beam angles

Different applications on a marine vessel or offshore platform require different beam angles, from general lighting on a deck that require a wide angle, to focussed lighting of safety-critical areas. As a result, the FL70 LED floodlight is available in 7 different beam angles of 18, 27, 39, 60, 80, 100 and 120 degrees.

Easy, time-saving installation

When it comes to installation, time is money. To make the installation quick and easy, the FL70 can be connected in groups of three, with one luminaire providing power to the other two, i.e. only one of the three luminaires requires a junction box. Many customers will also find the lightweight design (9 kg) an advantage when it comes to installation. Multiple connection options and an adjustable bracket further simplify the mounting and operation of the floodlight.

Robust and reliable

Floodlights can be critical in ensuring a safe working environment. Therefore, they need to be robust and reliable in all types of weather conditions. The FL70 floodlight is designed to operate in ambient temperatures between -35°C and +55°C. The seawater-resistant aluminium housing provides a protection rating of IP66/67.

For more information on the FL70 range of LED floodlights from Glamox, please visit www.glamox.com/offshore

About Glamox AS

Glamox is a Norwegian industrial group that develops, manufactures and distributes professional lighting solutions for the global market. The Glamox Group is a leading supplier to the world’s marine, onshore and offshore markets, and a significant supplier to the professional building market in Europe. 
 
The Glamox Group is a global organisation, with more than 2,400 employees within sales and production in several European countries, as well as Asia, North and South America. The turnover is NOK 3.1 billion. The Group owns a range of quality lighting brands including Glamox, Aqua Signal, Norselight, Luxo, LINKSrechts, Küttel, Luxonic and ES-SYSTEM. Glamox is committed to meeting customer needs and expectations by providing quality products and solutions, service and support. www.glamox.com

Captions for Photographs:

The FL70 range of LED floodlights from Glamox offer a system lifetime of 100,000 hours (L70B50) and require minimal maintenance.

The FL70 LED floodlights are available in 7 different beam angles to suit every offshore application.

Contact information

For more information, please contact:

Glamox International

Tel: +44 (0) 7719 547 175

Service.gi@glamox.com

www.glamox.com/gmo

Press Release Issued by:

Dean Palmer, Director, SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire PE9 1SW

Tel: +44 (1780) 764 254

Mobile: +44 (7703) 023771

dean@silverbulletpr.co.uk
www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.