| Date |  |
| --- | --- |
| 18th September 2018 | Page 1 of 1 |

# For immediate release

Safe communication with KUKA and KEB

Industry 4.0 combines production with the latest modern information technology and automation systems. This is based on intelligent, digitally linked systems that connect plant and machinery. KUKA and KEB Automation have developed a solution that demonstrates how this works in practice.

In this field, KEB Automation is offering a new solution for implementing connectivity to KUKA robots in various applications. With the C6 HMI LC, KEB now offers the possibility to both exchange data and to control and program the KUKA robot. The KEB system combines display, using an HMI, and control, via a PLC – in a single machine. This simplifies the complexity of the system and reduces costs. EtherCAT, as a powerful fieldbus, also facilitates connection to the robot.

Working from individual customer requirements, KEB offers several implementation solutions to suit a wide range of applications:

Visualisation

Using the C6 HMI LC, the user is able to display information – such as the current position of the robot – via a corresponding display concept and can exchange data between the robot and the HMI.

Control

The function module library “mxAutomation” from KUKA, which is based on PLC open standards, allows programming, diagnosis and manual operation of the KUKA robot via FB modules of the PLC. The library introduces almost all KUKA programming language commands into the PLC. Motion control of the axes is then performed by the robot itself.

Safety

In addition, the KEB solutions enable integration of safety controls to the system. The C6 Safety PLC from KEB uses “Safety-over-EtherCAT” as a secure fieldbus protocol for data transmission and communication with the robot, whereby safety functions can be implemented via the robot.

To view a video of the demonstration system, please visit: https://www.youtube.com/watch?v=DiSuYRue7qc

For more information, please visit www.keb.co.uk or visit us on stand 105 at the Robotics & Automation show (10-11 October 2018) at the ArenaMK in Milton Keynes.

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photographs and Captions:

KEB has developed a solution for implementing connectivity to KUKA robot applications 
(Photo: KEB Automation KG / KUKA KRC4).

### Contact information

For more information, please contact:

Mark Checkley

Sales & Marketing Manager,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (1780) 764 254

Mobile: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.