| Date |  |
| --- | --- |
| 28th May 2020 | Page 1 of 1 |

# For immediate release

KEB launches new spring-applied brake with reduced overall length and weight to suit disc motor applications

KEB Automation has launched a new spring-applied brake with reduced overall length and weight to suit disc motors and other applications where installation space is narrow or restricted.

The new COMBISTOP 38S spring-applied brake has an overall length which, depending on the size selected, is reduced by 2mm from 13.5mm to 11.5mm. The weight is also significantly lower compared to the Type 38N/H brake from KEB.

Hendrik Wieneke, Deputy Sales Manager, Magnet Technology at KEB comments: “The COMBISTOP 38S is ideally suited to disc motor applications. The weight and length reductions are decisive advantages for the customer, particularly when used in weight-sensitive applications.”

All torque-transmitting parts of the COMBISTOP 38S are manufactured in metal. In the five brake sizes (02 to 06), the brake is designed for rated torques from 5Nm up to 70Nm. Another key feature is a new generation of brake friction linings that are now available. Due to the flexibility of these friction linings, the brake can be adapted and optimised for specific applications.

The COMBISTOP 38S is interchangeable with the COMBISTOP 38 and is CSA-approved. A hand release option is also available, as well as flange, dust protection ring and a cold climate version (CCV).

The COMBISTOP range of brakes from KEB are electromagnetically actuated dual-surface spring-applied brakes for dry-running applications. The braking force is applied by the springs and released through the electromagnetic force. The brakes are tried and tested through millions of cycles and can be used wherever rotating masses need to be stopped or where shafts need to be held securely in a precise position. High quality materials together with high precision manufacturing, process inspections and functional testing guarantee reliable, safe operation.

On request, KEB can design the COMBISTOP brake to suit customer requirements; for example, the brake can be supplied with pre-mounted armature and increased torque.

For more information on KEB’s portfolio of brakes and other magnet technologies, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photographs and Captions:

The COMBISTOP 38S spring applied brake has reduced overall length and weight to suit disc motor applications.

### Contact information

For more information, please contact:

Mark Checkley

Sales & Marketing Manager,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (1780) 764 254

Mobile: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.