| Date |  |
| --- | --- |
| 8th July 2021 | Page 1 of 1 |

# For immediate release

KEB extends its COMBIVERT F6 range of drive controllers

KEB Automation has extended its COMBIVERT F6 range of high performance single-axis drive controllers with an even wider choice of power ratings from 2.2kW up to 450kW.

COMBIVERT F6 drive controllers are extremely compact, energy efficient and flexible for a wide variety of control applications in automated, safety-oriented machines. The drives provide optimal motor control in real time, as well as integrated safety functionality. Typical applications include materials handling, textiles, plastics, processing technology, machine tools, food and beverage processing and packaging, robotics, woodworking, and renewable energy systems (e.g. wind turbines).

Mark Checkley, Sales & Marketing Manager at KEB (UK) Ltd comments: “The extended power ranges will enable our UK customers to implement even more new machine concepts that require extended power, communication and integrated safety. In addition to the control of widely-supported motor types such as synchronous, asynchronous, permanent magnet, synchronous reluctance, linear, high-torque motors and high speed motors, the COMBIVERT F6 offers additional functions such as automatic anti-cogging and optimised torque pre-control for linear and non-linear kinematics. Motor operation with encoder feedback or encoderless ASCL/SCL for precise speed control is also possible.”

The COMBIVERT F6 range of drive controllers are 100% in-house designed and built by KEB Automation. The drives can be customised with a variety of design options to suit the specific application. Safety functionality can be selected in modules to suit the requirements of the machine. Ethernet-based bus systems can be switched via software, thus enabling flexible connection to higher-level control systems via EtherCAT, Profinet, Powerlink, Ethernet I/P or CAN.

Encoderless safety

The safe operation of machines often requires safety functions for monitoring speeds, directions of rotation or axis positioning. The PRO version of COMBIVERT F6 enables the implementation of encoderless safety. This means that safe solutions can be implemented, for example, in applications where no safe speed encoder can be installed on the motor. In addition to more individual machine concepts, encoderless safety functions also enable cost-effective, simple motion monitoring, as well as reduced effort in terms of maintenance and servicing. Integration of the safety fieldbus system Safety-over-EtherCAT (FSoE) plays a central role in machine designs. Conventional safety wiring is no longer required.

Flexible cooling to suit the application

The COMBIVERT F6 has a choice of four cooling options. These include an air-cooled built-in version (IP20) with an exchangeable fan; an air-cooled push-through version (rear side IP54) that allows waste heat to be removed from the control cabinet; a liquid-cooled built-in version with braking resistors and stainless steel piping; and a liquid-cooled push-through version with cooling liquid management (rear side IP54).

Optional accessories

A range of accessories are available for the COMBIVERT F6, including mains EMC filters, mains choke, ouptut chokes and filters, combi-filters (EMC/output choke), sine-wave filters, harmonic filters, sine-wave EMC filters, and high performance ferrite cores.

Start up and analysis software

KEB Automation also provides its easy-to-use software, COMBIVIS studio 6, for start up, administration and analysis. This includes start-up Wizards for quick and easy product configuration, direct access to device documentation, as well as enabling online drive parameter list comparisons and the set up of key safety indicators and functions. With a foundation built on libraries, devices and template databases, COMBIVIS studio 6 allows rapid, simple solutions to be generated for a wide range of applications.

For more information on the COMBIVERT F6 servo drive, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photographs and Captions:

The COMBIVERT F6 range of high performance servo drives has been extended to include power ranges from 2.2kW up to 450kW (Photo: KEB).

### Contact information

For more information, please contact:

Mark Checkley

Sales & Marketing Manager,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (1780) 764 254

Mobile: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.