| Date |  |
| --- | --- |
| 20th September 2022 | Page 1 of 1 |

# For immediate release

New electromagnetic brake from KEB is immune to remanence

If dynamic braking processes occur in an application, the housing of the brake becomes magnetically energised. This so-called remanence (residual magnetism) can lead to restrictions within the machine or system and consequently to increased costs. Due to a redesign of the COMBINORM B electromagentic brake from KEB Automation, remanence does not occur in the first place. In additon, the underlying mode of operation noticeably extends the service life of important components.

As an invisible force, brakes are responsible for starting, stopping, safe holding and positioning in numerous applications. Depending on the braking process, the housing of the brake may become magnetically energised (remanence). The more often a brake switches, the more self-remanence develops. As a result, the rotor on the brake is no longer powerful enough to rotate freely. The brake locks and the motor stops. Other consequences are increased wear and, in the worst case scenario, motor burnout, which can result in the entire machine or system coming to a standstill.

KEB has addressed this problem with the COMBINORM B brake, which is actuated by the operating voltage. The electromagnetic brake is the most economical solution for braking and holding loads for flange- and shaft-mounted installation in machines and systems.

### Anti-remanence function

The special feature of the COMBINORM B brake is the housing, which is divided into an inner and outer housing. As Simon Janke, Sales Brakes and Clutches at KEB explains: "We’ve developed the COMBINORM B as a powerful anti-remanence brake. For this, we rely on an artificially created air gap that prevents the armature part from sticking to the magnet. There are no effects on the torque."

Originally manufactured to a customer’s individual request, the brake with anti-remanence function is now available for use in a wide range of applications. "In addition to mail processing, the classic areas in which the brake is used include winding devices, door and gate systems, roller conveyors, balancing or sorting machines," states Janke. In addition, the COMBINORM B is also suitable as a solution for medical technology and packaging machines.

The anti-remanence property is not the only advantage the brake provides. It also offers short switching times, which contributes to increased safety in the machine. Furthermore, a wide temperature and voltage range is covered – the best conditions for use in as many areas as possible. For example, a high range of temperatures is often required in outdoor applications. This flexibility makes it possible to serve even very customer-specific applications. Backlash-free, maintenance-free and with a long service life, the COMBINORM B saves costs and, with its compact design, finds sufficient space in many applications.

COMBINORM B is available in voltages from 24V (special voltages on request) and in a torque range from 0.5 to 500Nm.

For more information on the COMBINORM B brake, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photographs and Captions:

Backlash-free, maintenance-free and with a long service life, the COMBINORM B electromagnetic brake cuts costs and with its compact design, can be installed in applications where space is limited.

The COMBINORM B brake is actuated by the operating voltage and is the most economical solution for braking and holding loads for flange- and shaft-mounted installation in machines and systems.

### Contact information

For more information, please contact:

Mark Checkley

Managing Director,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.