| Date |  |
| --- | --- |
| 17th January 2023 | Page 1 of 1 |

# For immediate release

E-buses: how auxiliary drives protect the environment

Conventional vehicles in urban traffic consume a large part of the energy for the auxiliary drives alone. In order to reduce emissions and costs, KEB Automation uses an inverter system for the electrification of air compressor, power steering pump and co. This enables buses to reach a new level of sustainability.

Electromobility can contribute to significant CO2 savings and pave the way to climate-neutral transport. More and more consumers are turning to environmentally friendly modes of transport. A change is also taking place in the area of commercial vehicles and mobile machinery. In addition to the main drives, electrification also affects the auxiliary drives in the vehicle, which include power steering pumps, air compressors, ventilation systems, CO2 heat pumps, transport cooling systems, hydraulic pumps and generator applications.

Electrified power take-offs are highly efficient, require comparatively little maintenance, are simple in design and are convincing in terms of torque output and low operating costs. Furthermore, users benefit from compact dimensions, low noise levels and reduced energy consumption, which increases the range of an electric bus, for example.

Inverter system with integrated UDS features

For reliable operation of the auxiliary units, KEB offers the approriate drives, controls and software solutions from a single source. For example, the T6 APD is a scalable and modular inverter system with integrated power electronics, intelligent mobile control unit and EMC filter solutions. The T6 system can be flexibly adapted to different vehicle requirements and enables the integration of up to six inverter modules, which are available in three power levels with rated output currents of 16.5A, 33A and 60A. Two CAN ports are available for communication, supporting all common CAN protocols such as J1939, CANopen, UDS (Unified Diagnostic Services) and many more.

Boris Schneider, team leader for E-mobility applications at KEB Automation comments: "The software of the T6 APD is modular and customisable. Users can choose from a pool of different apps for each inverter output. On the one hand, generic apps from KEB are available, but also apps directly from the aggregate manufacturer."

With the latest software version, the T6 APD now also supports the UDS diagnostic protocol on the CAN bus. Based on a collection of different services within the protocol, almost all available parameters can be read and written. Error memories can be read out or deleted. It is also possible to transfer files and software via the UDS interface.

The electrification of buses marks a step towards climate-neutral mobility. Especially in urban traffic, advantages such as the quiet operation of the auxiliary units come into their own. A better driving experience due to significantly less noticeable vibrations in the interior and the overall increased efficiency are further aspects that call for the electrification of main and auxiliary drives.

For more information, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photographs and Captions:

KEB’s T6 APD system enables integration of up to six inverter modules.

### Contact information

For more information, please contact:

Mark Checkley

Managing Director,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.