| Date |  |
| --- | --- |
| 28th September 2023 | Page 1 of 1 |

# For immediate release

Cutting, dosing and packing with safety drives

Fabian Fischer, Team Leader Application Sales at KEB Automation, explains the challenges food and packaging machinery pose for drive and automation solutions and how these can be overcome. Functional safety concepts, for example, are of particular importance.

Food and packaging applications are characterised by harsh environmental conditions. In many cases, the machines are cleaned with aggressive washing substances and high pressure. Motors, frequency inverters and controllers must therefore be robust and hard-wearing. The circuit boards in the current series of drive controllers from KEB Automation are equipped with a protective lacquer specially developed for these environments. HMI control panels from KEB are made from stainless steel and are protected to IP69K. High pressure cleaning and even temperatures up to 50°C do not affect the devices. Performance is also important: food and packaging machines must ensure precise cutting, dosing, mixing and filling in the shortest of cycle times. For this purpose, KEB offers compact, energy-saving, dynamic drives with high overloads and precise control.

Functional safety from drives
Up to now, safety technology was often set up decentrally with external safety modules. These were expensive, complex to wire and required space in the control cabinet. KEB builds functional safety concepts in a smart way. Functions such as “Safe Torque Off” (STO) or “Safely-Limited Speed” (SLS) are integrated in the COMBIVERT range of drive controllers and can be selected on a modular basis. Wiring is not required if a safety controller with, for example, Safety over EtherCAT or PROFIsafe is used. With many speed-based safety functions, the safe encoder can even be eliminated. With KEB’s integrated safety function “Safe Door-Lock Control” (SDLC) door switches on food processing machines with knife drives, for example, are only released when the knife has come to a standstill. An external module for monitoring is not necessary.

Complete system solutions
From HMIs, controls and drives, to motors, brakes and clutches, KEB implements drive solutions from a single source. Individual components are optimally matched to each other, resulting in maximum machine efficiency. As, for example, the motor and drive controller harmonise perfectly, KEB also complies with the new IE2 energy efficiency label according to the EN 61800-9-2 standard. Another advantage for the machine builder is that there is only one contact person required for all matters concerning the drive. The flexibility of interfaces to components from third-party suppliers is retained in all this, in order to integrate components effortlessly into existing systems.

For more information, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photos and captions:

With the COMBIVERT series from KEB, safety functions are integrated in the drive controllers.

### Contact information

For more information, please contact:

Mark Checkley

Managing Director,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.