| Date |  |
| --- | --- |
| 9th January 2024 | Page 1 of 1 |

# For immediate release

Two-in-one motor with integrated frequency inverter from KEB Automation

By using frequency inverters, plant and machine manufacturers can get even more out of their motors. This is because they allow universal drive machines to be operated flexibly. With this in mind, KEB Automation has expanded its product portfolio: asynchronous geared motors with integrated frequency inverters – an efficient and convenient 2-in-1 motor solution for a wide range of applications.

When it comes to targeted starting and stopping, smooth starting and braking, or operating the motor at different speeds, frequency inverters are the first choice. Drive controllers from KEB Automation are at home in machines and plants across the world, where they ensure smooth drive operation. In addition to the previous range of these central drive controllers, decentralised solutions are also now available. Specifically, the MU series inverters are designed so that they can be used as an integral component of KEB geared motors with a power range from 0.37 kW to 7.5 kW.

Daniel Lehmann, Product Manager Motors at KEB Automation, explains the benefits of the motor-inverter combination: "The inverters are mounted directly on the motor as decentralised devices. This saves important space in the control cabinet. Users also benefit from high performance and easier installation."

Depending on the performance requirements, the application and the customer’s needs, the KEB portfolio offers a customised solution. "We offer our gear units and motors according to the modular principle. The same applies to motors with integrated inverters. Here, asynchronous geared motors can be combined with different frequency inverters and technical specifications," adds Lehmann.

Flexible, custom drives
The integrated frequency inverters are available in ten sizes for mains voltages of 230 and 400 V. The motors can be efficiently designed for different operating points (87, 100 and 120 Hz). This means that customised drives can be put together flexibly. Short cable lengths also prove to be particularly practical in daily operation. In addition to the drive task, the 2-in-1 motors can also take on control and monitoring functions and can be integrated into centrally controlled systems.

Motors with integrated inverters are in demand in intralogistics, textiles, wood and metal processing machines. Food and packaging machines also benefit from the fact that the inverters are protected by a separate housing for use in the field. "The inverters have a high IP protection class and are designed for ambient temperatures of up to 40 degrees Celsius. EMC limit class C2 in accordance with DIN EN 61800-3 ensures smooth operation, with motor installation and standard switching frequency," says Lehmann.

Create your own drive

KEB Automation offers the ideal ‘power’ for numerous applications. But which motor is ideal for your machine? Which gear units is suitable for your system? The KEB-DRIVE configuration software helps you with these questions and assists you in the selection of gear units and motors. You can also receive 3D models and detailed technical descriptions.

For more information, please visit www.keb.co.uk

About KEB Automation KG

KEB provides a complete Automation Solution from gear shaft to HMI screen, including motion control up to CNC level, safety systems with FsoE (Failsafe over EtherCAT) and visualisation. KEB’s aim is always to find the optimum drive and control solution tailored to suit a customer’s precise requirements.

Headquartered in Barntrup, Germany, KEB is a medium-sized global business with a workforce in excess of 1,400 worldwide, with more than 10% of these working in research and development. With structured growth over the last 40 years, the company’s motto is ‘reliability creates trust’. Every day, the quality and performance levels of KEB solutions are reflected in its customers’ machines and installations.

KEB group consists of 10 subsidiary companies worldwide, including KEB (UK) Ltd. and Sales & Service Centres in a further 23 countries to support its growing customer base.

Photos and captions:

The 2-in-1 motor solution from KEB. The inverters are mounted directly on the motor as decentralised devices.

### Contact information

For more information, please contact:

Mark Checkley

Managing Director,

KEB (UK) Ltd.

5 Morris Close,

Park Farm Industrial Estate,

Wellingborough, Northants, NN8 6XF

Tel: +44 (0) 1933 402 220

Mobile: +44 (0) 7810 568056

Email: mark.checkley@keb.co.uk

Website: www.keb.co.uk

Press Release Issued by:

Dean Palmer,
Director,
SilverBullet PR Ltd, 
19, Glen Crescent, Stamford,

Lincolnshire, UK.
PE9 1SW

Tel: +44 (7703) 023771

Email: dean@silverbulletpr.co.uk

Website: www.silverbulletpr.co.uk

High resolution images are available on request from SilverBullet PR.