Laser line scanner generates 3D profiles of complex gear teeth

Engineering company EHR is using Micro-Epsilon’s scanCONTROL 2800-25 laser line scanner to check the run-out characteristics of complex gear teeth. The laser line scanner generates a digital 3D profile of the gear tooth area. After inspection of this profile, the workpiece can be adjusted if required.

Gear shafts with plug-in teeth, bevel gears and hypoid teeth and other similar axial components can warp during manufacture. Therefore, an inspection of the run-out is required. After inspection, the workpiece can be adjusted if required. In order to adjust the workpiece, the extent of the ‘ovality’ and the direction of adjustment need to be determined. EHR’s optical measurement system was developed specifically for this purpose, enabling rapid, extremely precise automated straightening of the workpiece.

The scanCONTROL 2800-25 is aligned with the component in such a way that the laser line is perpendicular to the gear teeth. When rotating the clamped component, the entire tooth area is shown digitally in 3D. This 3D point cloud is then evaluated according to customer requirements. In order to make a comparison with tactile dislocation, computer-generated digital balls are placed between the flanks of the teeth.

Another benefit of using ‘digital dislocation’ is that the diameter of the ball can be changed quickly and easily. All ball diameters that should pass between the gear teeth can be selected using simple configuration tools. Due to this increase in the number of evaluation results, measurement accuracy of better than 5(m is achieved, which is lower than the measurement resolution of the laser scanner.

The scanCONTROL 2800-25 comprises a compact sensor and an intelligent controller, which are connected by a cable. The controller outputs both the 2D profile information as well as analysed data. The integrated FireWire/Ethernet interface enables complete control for multiple scanCONTROL systems via a PC, as well as high data rates.

A profile generated by the scanCONTROL 2800 consists of a maximum of 1,024 points and a calibrated measurement value each for X and Z. These points are acquired simultaneously across the entire line and made immediately available to a PC for a real time evaluation of the profile. The sensor provides a profile frequency of 4,000Hz and up to 256,000 measuring points per second.

For more information on Micro-Epsilon’s scanCONTROL 2800 range of laser line scanners, please call the sales department on 0151 355 6070 or email: info@micro-epsilon.co.uk

– ENDS – [401 words]

Note to Editors: Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of displacement sensors measure everything from to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include 1D, 2D and even 3D laser-optical sensors and systems, eddy-current, capacitive, LVDT & inductive, potentiometric and draw-wire principles.  Additionally Micro Epsilon has developed its own range of non-contact infrared temperature sensors that can measure virtually any target temperature from -40 to +3,300°C.

With more than 30 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its customers.

To download high resolution images for this article, please go to the “Press Area” at www.silverbulletpr.co.uk . Alternatively, you can request an image by contacting:

Issued by:			Dean Palmer

Director

SilverBullet PR Ltd

Frith Farm, Ryhall Road, Tolethorpe, Stamford,

Lincolnshire, PE9 4BJ.

Tel: 01780 753 000

Mobile: 07703 023771

Email: dean@silverbulletpr.co.uk

Reader Enquiries/Advertising:	Chris Jones
				Managing Director

Micro-Epsilon UK Ltd

Unit 1, Pioneer Business Park
North Road
Ellesmere Port
Cheshire CH65 1AD
Tel: +44 (0) 151 355 6070
Fax: +44(0) 151 355 6075

Mobile: 07789 484503

Email: chris.jones@micro-epsilon.co.uk

# Text boxes

#### Ref. ME124									                     8th June 2011