Micro-Epsilon to showcase its colour sensors at Advanced Engineering 2018

At the Advanced Engineering Show (31st October – 1st November 2018) at the NEC, Birmingham, Micro-Epsilon UK (stand F40) will showcase its full range of sensor technologies, including non-contact capacitive, eddy current and laser triangulation displacement sensors, as well as 2D/3D laser profile sensors, thermal imagers and colour sensors. In addition, the stand will feature five interactive product demonstrations, including two colour measurement systems:

For those with a need to measure colour, the stand will feature a demonstration of the colorCONTROL ACS7000, an inline high speed colour measurement system that measures the actual colour of the target by identifying their coordinates in the colour space. The system can be set up to continually monitor a production process and output the colour measurement via Ethernet, EtherCAT or RS422. The demonstration system will show how precisely the colorCONTROL ACS7000 detects the colour and intensity of a wide range of targets mounted on a turntable. Not only does the system recognise colours via a reference value (colour comparison), it also ensures unique identification and measurement of all colours via the reflection spectrum. The demonstration shows how light intensity, surfaces/textures, and different materials influence the colour measurement.

### True colour recognition

Visitors can also see a demonstration of the new colorSENSOR CFO200, a colour recognition sensor designed for high precision true colour measurement in industrial applications. The sensors stand out due to their high colour accuracy, good reproducibility, high measuring rate and modern communications interfaces for easier network integration and Industry 4.0 capability. The CFO200 is suitable for a wide range of applications including colour sorting tasks in food packaging (e.g. crown caps and labels), colour inspection of interior parts in the automotive industry, recognition of colour marks in the printing industry, quality control in packaging, cosmetics, medicine and plastic products.

### Measuring gaps and edges

Also on the stand is a demonstration of the gapCONTROL non-contact laser profile scanner. This sensor is designed specifically for the measurement of gaps and edges. Users can quickly and easily set up and configure the scanner without requiring any specific knowledge or programming skills. Typical applications include measuring flushness, proximity, gap width and depth, height differences, centre position, angle, collision avoidance and overlapping edges. The latest additions to the gapCONTROL series, the 2611 and 2911, are even more compact and provide additional functionality including the ability to measure even smaller gaps.

### Injection moulding temperature control

The moldCONTROL inline thermography system detects variations in quality by using a high speed, high resolution infrared thermal imaging camera. It records the entire component in up to six different views and examines it. The principle is simple: a thermoIMAGER TIM thermal imaging camera records the infrared radiation emanating from the mould and visualises it. The temperature distribution provides a quality statement about incorrect temperature control of the mould, malfunction of the tool temperature, visible geometry errors and hidden defects. On the stand, the demonstration involves the temperature measurement of plastic injection moulded LEGO bricks.

### Laser triangulation at its best

Visitors can see a demonstration of the optoNCDT 1420 laser displacement sensor. The speed, size, performance and ease of integration of these sensors is unrivalled in the market today. The sensors are suitable for a variety of medium-to-high volume applications in automation, machine building and systems integration, particularly where conventional laser sensors have reached the limits of their performance capabilities. The sensors are extremely compact, lightweight and so can be mounted in tight spaces on machines or other difficult-to-access locations. Designed for high precision, high speed, dynamic displacement, distance and position measurement applications, the sensors offer an adjustable measuring rate up to 4kHz and an excellent price-performance ratio, particularly for high volume OEM applications.

For more information or to book an appointment on the stand, please call the Micro-Epsilon sales department on 0151 355 6070 or email info@micro-epsilon.co.uk

– ENDS – [633 words]

Note to Editors: Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of displacement sensors measure everything from to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include 1D, 2D and even 3D laser-optical sensors and systems, eddy-current, capacitive, LVDT & inductive, potentiometric and draw-wire principles.  In addition, Micro Epsilon has developed its own range of non-contact infrared temperature sensors that can measure virtually any target temperature from -40 to +3,300°C. The company also manufactures a comprehensive range of colour recognition sensors.

With more than 45 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its customers.

To download high resolution images for this article, please go to www.silverbulletpr.co.uk/press . Alternatively, you can request an image by contacting:

Issued by:			Dean Palmer

Director

SilverBullet PR Ltd

19, Glen Crescent, Stamford,

Lincolnshire PE9 1SW

Tel: 01780 754 254

Mobile: 07703 023771

Email: dean@silverbulletpr.co.uk

Reader Enquiries/Advertising:	Louise Dodd,

Marketing Manager, 
Micro-Epsilon UK Ltd

1, Shorelines Building,
Shore Road, Birkenhead
Cheshire CH41 1AU
Tel: +44 (0) 151 355 6070
Fax: +44(0) 151 355 6075

Email: louise.dodd@micro-epsilon.co.uk

# Text boxes

#### Ref. ME329								                        27th September 2018