New PCIe interface card enables synchronous capture of digital sensor signals and encoder data

Precision sensor manufacturer Micro-Epsilon has introduced a new interface card for PCs that enables absolute synchronous capture of digital sensor signals and encoder data.

The IF2008 PCIe interface card from Micro-Epsilon is designed for installation in PCs with PCI Express interface slots. Absolute synchronous data acquisition plays an important role in measurement applications, particularly for planarity and thickness measurement tasks. The IF2008 PCIe interface card enables the synchronous capture of four digital sensor signals and two encoders. The data is stored in a FIFO memory in order to allow resource-saving processing in the PC in blocks.

In addition, the IF2008E expansion board offers two sensor inputs, two ADC inputs, four optocoupler inputs and four optocoupler outputs. Using both cards, a total of six digital sensors, two analogue sensors and two encoders can be connected for synchronous measurements.

For more information on the IF2008PCle interface card, please call the Micro-Epsilon sales department on 0151 355 6070 or email info@micro-epsilon.co.uk

– ENDS – [172 words]

Photos and captions:

The IF2008 PCIe interface card is installed in PCs with PCI Express expansion slots.

Note to Editors: Micro-Epsilon (www.micro-epsilon.co.uk) is a major global manufacturer of sensors, headquartered in Germany. The company’s range of displacement sensors measure everything from to distance, position, vibration, dimensions and thickness, using both contact and non-contact measurement techniques. These techniques include 1D, 2D and even 3D laser-optical sensors and systems, eddy-current, capacitive, LVDT & inductive, potentiometric and draw-wire principles.  In addition, Micro Epsilon has developed its own range of non-contact infrared temperature sensors that can measure virtually any target temperature from -40 to +3,300°C. The company also manufactures a comprehensive range of colour recognition sensors.

With more than 45 years’ experience in the industry, Micro-Epsilon isn’t just a sensor manufacturer. The company is highly innovative and understands the importance of providing complete solutions and support services for its customers. The firm is renowned for its expertise in consulting, development and application of industrial sensors to complex, customer-specific solutions for measurement, inspection and automation. The focus is on selling technical advantage to its customers.

To download high resolution images for this article, please go to www.silverbulletpr.co.uk/press . Alternatively, you can request an image by contacting:

Issued by:			Dean Palmer

Director

SilverBullet PR Ltd

19, Glen Crescent, Stamford,

Lincolnshire PE9 1SW

Tel: 01780 754 254

Mobile: 07703 023771

Email: dean@silverbulletpr.co.uk

Reader Enquiries/Advertising:	Jenny Croft,

Marketing Executive, 
Micro-Epsilon UK Ltd

1, Shorelines Building,
Shore Road
Birkenhead
Cheshire CH41 1AU
Tel: +44 (0) 151 355 6070
Fax: +44(0) 151 355 6075

Email: jenny.croft@micro-epsilon.co.uk

# Text boxes

#### Ref. ME347								                          3rd September 2019