Schaeffler at Hannover Messe 2019 (Hall 22, stand D43)

Schaeffler helps gearbox manufacturers reduce number of different parts

- Schaeffler has developed interchangeable gearbox bearing solutions to meet different requirements in the same design envelope

- Identical outside dimensions reduce component variations, particularly for shafts, housings and housing covers

- Economies-of-scale significantly reduce manufacturing costs

SUTTON COLDFIELD, UK, April 09, 2019. Gearbox manufacturers provide modular product portfolios by offering different numbers of gear teeth, gear stages that allow flexible combinations, and by varying the number of planetary gears. The speeds and loads on gearbox components such as gear teeth, shafts and bearings vary according to the application. Depending on the gearbox configuration and the associated requirements in terms of rigidity and load carrying capacity, bearings with different dimensions must then be implemented in a single bearing position, which requires a wide variety of housings, housing covers, gears and shafts.

The objective of Schaeffler’s new concept is to allow bearings of different designs but with identical dimensions to be implemented in one (i.e. the same) bearing position for various gearbox configurations. These “interchangeable gearbox bearing solutions” will be available based on dimension series 18 for high precision servo planetary gearboxes. For example, FAG deep groove ball bearings from series 618, INA angular contact ball bearings from series 718, and INA SGL angular contact roller bearings, allow the bearing support’s load carrying capacity, speed range and rigidity to be adjusted while retaining the same design envelope. Of the three variants, the INA SGL angular contact roller bearings offer the highest level of rigidity, which allows extremely rigid bearings and drives with very high positional accuracy to be achieved.

Identical outside dimensions eliminate the need for special adapters and component variations, particularly for the shafts, housings and housing covers. The associated development steps such as drawing modifications and NC programming in the manufacturing process, are no longer required. The reduction of gear, shaft and housing variants means higher production volumes, lower unit costs and faster deliveries.

Modular solution for planetary gear bearings

The design envelope and rigidity requirements of planetary gears means they are often supported by cylindrical rolling bearings without an outer ring. Both full-complement designs and designs with cages are used here, depending on the required load carrying capacity and speed, but these bearings are not interchangeable because their envelope circle diameters are different. As a result, new planetary gears must be designed, produced and mounted. To make interchangeable bearing solutions available, even for planetary gear bearing supports, Schaeffler’s design engineers have developed the INA RSLK1822, RSLK1830, and RSLK1850 cylindrical rolling bearings with cages based on the dimensions of full-complement RSL bearings. These feature identical outside dimensions and so can be used as replacements without any structural changes, design adjustments or additional outlay in terms of time and costs.

For more information, please contact Schaeffler UK’s Marketing Department on info.uk@schaeffler.com

Pictures: Schaeffler

Lower costs for modular gearbox systems: gearbox bearings in different designs but with identical outside dimensions, allow bearing supports to be optimised in terms of load carrying capacity, speed range and rigidity.

About Schaeffler

The Schaeffler Group is a global automotive and industrial supplier. By delivering high-precision components and systems in engine, transmission, and chassis applications, as well as rolling and plain bearing solutions for a large number of industrial applications, the Schaeffler Group is already shaping “Mobility for tomorrow” to a significant degree. The technology company generated sales of approximately 14.2 billion Euros in 2018. With around 92,500 employees, Schaeffler is one of the world’s largest family companies and, with approximately 170 locations in over 50 countries, has a worldwide network of manufacturing locations, research and development facilities, and sales companies. With more than 2,400 patent registrations in 2018, Schaeffler is Germany’s second most innovative company according to the DPMA (German Patent and Trademark Office).

|  | Schaeffler |  | Twitter |  | Facebook |  | Youtube |
| --- | --- | --- | --- | --- | --- | --- | --- |

Follow us on Twitter @SchaefflerUK and Twitter @schaefflergroup to get all of our latest press releases and news.

Contact:

Dean Palmer, Director, SilverBullet PR Ltd, Stamford, Lincolnshire, UK.

Tel. 07703 023771, email: dean@silverbulletpr.co.uk